## Slide 1: Hidden and Exposed Terminal Problem

## Slide 3: Near and far terminal problem-a person standing closer to somebody could always speak louder than a person further away

## Slide 4: Mobile IP

## Slide 6: Motivation for Mobile IP
Routing
based on IP destination address, network prefix (e.g. 129.13.42) determines physical subnet
change of physical subnet implies change of IP address to have a topological correct address (standard IP) or needs special entries in the routing tables
Specific routes to end-systems?
change of all routing table entries to forward packets to the right destination
does not scale with the number of mobile hosts and frequent changes in the location, security problems
Changing the IP-address?
adjust the host IP address depending on the current location
almost impossible to find a mobile system, DNS updates take to long time
TCP connections break, security problems

## Slide 7: Requirements to Mobile IP
Transparency
mobile end-systems keep their IP address
continuation of communication after interruption of link possible
point of connection to the fixed network can be changed
Compatibility
support of the same layer 2 protocols as IP
no changes to current end-systems and routers required
mobile end-systems can communicate with fixed systems
Security
authentication of all registration messages
Efficiency and scalability
only little additional messages to the mobile system required (connection typically via a low bandwidth radio link)
world-wide support of a large number of mobile systems in the whole Internet

## Slide 8: Terminology
Mobile Node (MN)
system (node) that can change the point of connection to the network without changing its IP address
Home Agent (HA)
system in the home network of the MN, typically a router
registers the location of the MN, tunnels IP datagrams to the COA
Foreign Agent (FA)
system in the current foreign network of the MN, typically a router
forwards the tunneled datagrams to the MN, typically also the default router for the MN
Care-of Address (COA)
address of the current tunnel end-point for the MN (at FA or MN)
actual location of the MN from an IP point of view
can be chosen, e.g., via DHCP
Correspondent Node (CN)
communication partner

## Slide 9: Example network
mobile end-system
Internet
router
router
router
end-system
FA
HA
MN
home network
foreign network
(physical home network
for the MN)
(current physical network for the MN)
CN

## Slide 10: Data transfer to the mobile system
Internet
sender
FA
HA
MN
home network
foreign
network
receiver
1
2
3
1. Sender sends to the IP address of MN,
HA intercepts packet (proxy ARP)
2. HA tunnels packet to COA, here FA,
by encapsulation
3. FA forwards the packet to the MN
CN

## Slide 11: Data transfer from the mobile system
Internet
receiver
FA
HA
MN
home network
foreign network
sender
1
1. Sender sends to the IP address of the receiver as usual, FA works as default router
CN

## Slide 12: Overview
CN
router
HA
router
FA
Internet
router
1.
2.
3.
home
network
MN
foreign
network
4.
CN
router
HA
router
FA
Internet
router
home
network
MN
foreign
network
COA

## Slide 13: Network integration
Agent Advertisement
HA and FA periodically send advertisement messages into their physical subnets
MN listens to these messages and detects, if it is in the home or a foreign network (standard case for home network)
MN reads a COA from the FA advertisement messages
Registration (always limited lifetime!)
MN signals COA to the HA via the FA, HA acknowledges via FA to MN
these actions have to be secured by authentication
Advertisement
HA advertises the IP address of the MN (as for fixed systems), i.e. standard routing information
routers adjust their entries, these are stable for a longer time (HA responsible for a MN over a longer period of time)
packets to the MN are sent to the HA,
independent of changes in COA/FA

## Slide 14: Agent advertisement
type = 16
length = 6 + 4 * #COAs
R: registration required
B: busy, no more registrations
H: home agent
F: foreign agent
M: minimal encapsulation
G: GRE encapsulation
r: =0, ignored (former Van Jacobson compression)
T: FA supports reverse tunneling
reserved: =0, ignored
preference level 1
router address 1
#addresses
type
addr. size
lifetime
checksum
COA 1
COA 2
type = 16
sequence number
length
0
7
8
15
16
31
24
23
code
preference level 2
router address 2
. . .
registration lifetime
. . .
R
B
H
F
M
G
r
reserved
T

## Slide 15: Agent Solicitation
If no agent advertisements are present or the inter-arrival time is too high, and an MN has not received a COA by other means, e.g., DHCP , the mobile node must send agent solicitations.
Care must be taken to ensure that these solicitation messages do not flood the network, but basically an MN can search for an FA endlessly sending out solicitation messages.
Typically, a mobile node can send out three solicitations, one per second, as soon as it enters a new network.
If a node does not receive an answer to its solicitations it must decrease the rate of solicitations exponentially to avoid flooding the network until it reaches a maximum interval between solicitations (typically one minute).
After these steps of advertisements or solicitations the MN can now receive a COA, either one for an FA or a co-located COA.
After these steps of advertisements or solicitations the MN can now receive a COA, either one for an FA or a co-located COA. The MN knows its location (home network or foreign network) and the capabilities of the agent (if needed).
The next step for the MN is the registration with the HA if the MN is in a foreign network.

## Slide 16: Registration-Having received a COA, the MN has to register with the HA. The main purpose of the registration is to inform the HA of the current location for correct forwarding of packets. Registration can be done in two different ways depending on the location of the COA.
t
MN
HA
registration
request
registration
reply
t
MN
FA
HA
registration
request
registration
request
registration
reply
registration
reply
The HA now sets up a mobility binding containing the mobile node’s home IP address and the current COA. Additionally, the mobility binding contains the lifetime of the registration. Registration expires automatically after the lifetime and is deleted; so, an MN should reregister before expiration.
If the COA is co-located, registration can be simpler. if the MN received an agent advertisement from the FA it should register via this FA if the R bit is set in the advertisement.

## Slide 17: Mobile IP registration request
home agent
home address
type = 1
lifetime
0
7
8
15
16
31
24
23
T x
identification
COA
extensions . . .
S
B
D
M
G
r
The first field type is set to 1 for a registration request.

## Slide 18: Mobile IP registration request
8.18
home agent
home address
type = 1
lifetime
0
7
8
15
16
31
24
23
T x
identification
COA
extensions . . .
S
B
D
M
G
r
S: simultaneous bindings-MN can specify if it wants the HA to retain prior mobility bindings.
B: broadcast datagrams-denote the requested behavior for packet forwarding. Setting the B bit generally indicates that an MN also wants to receive the broadcast packets which have been received by the HA in the home network.
D: decapsulation by MN -If an MN uses a co-located COA, it also takes care of the decapsulation at the tunnel endpoint.
M mininal encapsulation
G: GRE encapsulation
r: =0, ignored
T: reverse tunneling requested
x: =0, ignored
UDP packets are used for registration requests. The IP source address of the packet is set to the interface address of the MN, the IP destination address is that of the FA or HA (depending on the location of the COA).
UDP is used because of low overheads and better performance
compared to TCP in wireless environments.
The first field type is set to 1 for a registration request.

## Slide 19: Mobile IP registration reply
home agent
home address
type = 3
lifetime
0
7
8
15
16
31
code
identification
extensions . . .
Example codes:
registration successful
0 registration accepted
1 registration accepted, but simultaneous mobility bindings unsupported
65 administratively prohibited
66 insufficient resources
67 mobile node failed authentication
68 home agent failed authentication
69 requested Lifetime too long
registration denied by HA
129 administratively prohibited
131 mobile node failed authentication
133 registration Identification mismatch
135 too many simultaneous mobility bindings

## Slide 20: Mobile IP registration reply
8.20
home agent
home address
type = 3
lifetime
0
7
8
15
16
31
code
identification
extensions . . .
Example codes:
registration successful
0 registration accepted
1 registration accepted, but simultaneous mobility bindings unsupported
65 administratively prohibited
66 insufficient resources
67 mobile node failed authentication
68 home agent failed authentication
69 requested Lifetime too long
registration denied by HA
129 administratively prohibited
131 mobile node failed authentication
133 registration Identification mismatch
135 too many simultaneous mobility bindings
The home address is the
fixed IP address of the MN, home agent is the IP address of the HA, and COA
represents the tunnel endpoint. The 64 bit identification is generated by the MN to identify a request and match it with registration replies. This field is used
for protection against replay attacks of registrations. The extensions must at
least contain parameters for authentication.
A registration reply, which is conveyed in a UDP packet, contains a type field set to 3 and a code indicating the result of the registration request.

## Slide 21: Encapsulation
Describes the mechanisms used for forwarding packets between the HA and the COA.
A tunnel establishes a virtual pipe for data packets between a tunnel entry and a tunnel endpoint. Packets entering a tunnel are forwarded inside the tunnel and leave the tunnel unchanged. Tunneling, i.e., sending a packet through a tunnel, is achieved by using encapsulation.
Encapsulation is the mechanism of taking a packet consisting of packet header and data and putting it into the data part of a new packet. The reverse operation, taking a packet out of the data part of another packet, is called decapsulation.

## Slide 22: Encapsulation- describes exactly what the HA at the tunnel entry does. The HA takes the original packet with the MN as destination, puts it into the data part of a new packet and sets the new IP header in such a way that the packet is routed to the COA. The new header is also called the outer header for obvious reasons. Additionally, there is an inner header which can be identical to the original header as this is the case for IP-in-IP encapsulation, or the inner header can be computed during encapsulation.
original IP header
original data
new data
new IP header
outer header
inner header
original data
IP-in-IP encapsulation

## Slide 23: Encapsulation I
IP-in-IP-encapsulation
  tunnel between HA and COA
The version field ver is 4 for IP version 4,
the internet header length (IHL) denotes the length of the outer header in 32 bit words.
DS(TOS) is just copied from the inner header
the length field covers the complete encapsulated packet. The fields up to TTL are set according to RFC 791 for mobile IP.
TTL must be high enough so the packet can reach the tunnel endpoint.
IP-in-IP, is the type of the protocol used in the IP payload. This
field is set to 4, the protocol type for IPv4 because again an IPv4 packet follows after this outer header.
IP checksum is calculated as usual. The next fields are
the tunnel entry as source address (the IP address of the HA) and the tunnel exit point as destination address (the COA).
Care-of address COA
IP address of HA
TTL
IP identification
IP-in-IP
IP checksum
flags
fragment offset
length
DS (TOS)
ver.
IHL
IP address of MN
IP address of CN
TTL
IP identification
lay. 4 prot.
IP checksum
flags
fragment offset
length
DS (TOS)
ver.
IHL
TCP/UDP/ ... payload

## Slide 24: Encapsulation II
Minimal encapsulation (optional)
  avoids repetition of identical fields
  e.g. TTL, IHL, version, DS (RFC 2474, old: TOS)
  only applicable for unfragmented packets, no space left for fragment identification
If the S bit is set, the original sender address of the CN is included as omitting the source is quite often not an option.
care-of address COA
IP address of HA
TTL
IP identification
min. encap.
IP checksum
flags
fragment offset
length
DS (TOS)
ver.
IHL
IP address of MN
original sender IP address (if S=1)
S
lay. 4 protoc.
IP checksum
TCP/UDP/ ... payload
reserved

## Slide 25: Generic routing encapsulation (GRE)
Allows the encapsulation of packets of one protocol suite into the payload portion of a packet of another
protocol suite.
the left side the fields of a packet inside the tunnel between home agent and COA using GRE as an encapsulation scheme. The outer header is the standard IP header with HA as source address and COA as destination address.
original
header
original data
new data
new header
outer header
GRE header
original data
original header

## Slide 26: Generic Routing Encapsulation
Care-of address COA
IP address of HA
TTL
IP identification
GRE
IP checksum
flags
fragment offset
length
DS (TOS)
ver.
IHL
IP address of MN
IP address of CN
TTL
IP identification
lay. 4 prot.
IP checksum
flags
fragment offset
length
DS (TOS)
ver.
IHL
TCP/UDP/ ... payload
routing (optional)
sequence number (optional)
key (optional)
offset (optional)
checksum (optional)
protocol
rec.
rsv.
ver.
C
R
K
S
s
RFC 1701
RFC 2784
reserved1 (=0)
checksum (optional)
protocol
reserved0
ver.
C
The protocol type used in this outer IP header is 47 for GRE.
The C bit indicates if the checksum field is present and contains valid information. If C is set, the checksum field contains a valid IP checksum of the GRE header and the payload.
The R bit indicates if the offset and routing fields are present and contain valid information.
The offset represents the offset in bytes for the first source
routing entry. The routing field, if present, has a variable length and contains fields for source routing. If the C bit is set, the offset field is also present and, vice versa, if the R bit is set, the checksum field must be present. The only reason for this is to align the following fields to 4 bytes. The checksum field is valid only if C is set, and the offset field is valid only if R is set respectively.
GRE also offers a key field which may be used for authentication. If this field is present, the K bit is set. However, the authentication algorithms are not further specified by GRE.
The sequence number bit S indicates if the sequence number field is present,
if the s bit is set, strict source routing is used.
The recursion control field (rec.) is an important field that additionally distinguishes GRE from IP-in-IP and minimal encapsulation. This field represents a counter that shows the number of allowed recursive encapsulations. As soon as a packet arrives at an encapsulator it checks whether this field equals zero. If the
field is not zero, additional encapsulation is allowed – the packet is encapsulated and the field decremented by one. Otherwise the packet will most likely be discarded. This mechanism prevents indefinite recursive encapsulation which might happen with the other schemes if tunnels are set up improperly (e.g., several
tunnels forming a loop). The default value of this field should be 0, thus allowing only one level of encapsulation.
The following reserved fields must be zero and are ignored on reception. The version field contains 0 for the GRE version.

## Slide 27: Optimization of packet forwarding
Triangular Routing
sender sends all packets via HA to MN
higher latency and network load
“Solutions”
sender learns the current location of MN
direct tunneling to this location
HA informs a sender about the location of MN
big security problems!
Change of FA
packets on-the-fly during the change can be lost
new FA informs old FA to avoid packet loss, old FA now forwards remaining packets to new FA
this information also enables the old FA to release resources for the MN
Although the computers might be only meters away, the packets have to travel around the world! This inefficient behavior of a nonoptimized mobile IP is called triangular routing. The triangle is made of the three segments, CN to HA, HA to COA/MN, and MN back to CN.

## Slide 28
One way to optimize the route is to inform the CN of the current location of the MN. The CN can learn the location by caching it in a binding cache which is a part of the local routing table for the CN. The appropriate entity to inform the CN of the location is the HA. The optimized mobile IP protocol needs four additional messages.
● Binding request: Any node that wants to know the current location of an MN can send a binding request to the HA. The HA can check if the MN has allowed dissemination of its current location. If the HA is allowed to reveal the location it sends back a binding update.
● Binding update: This message sent by the HA to CNs reveals the current location of an MN. The message contains the fixed IP address of the MN and the COA. The binding update can request an acknowledgement.
● Binding acknowledgement: If requested, a node returns this acknowledgement after receiving a binding update message.
● Binding warning: If a node decapsulates a packet for an MN, but it is not the current FA for this MN, this node sends a binding warning. The warning contains MN’s home address and a target node address, i.e., the address of the node that has tried to send the packet to this MN. The recipient of the warning then knows that the target node could benefit from obtaining a fresh binding for the MN. The recipient can be the HA, so the HA should now send a binding update to the node that obviously has a wrong COA for the MN.

## Slide 29: Change of foreign agent
CN
HA
FAold
FAnew
MN
MN changes location
t
Data
Data
Data
Update
ACK
Data
Data
Registration
Update
ACK
Data
Data
Data
Warning
Request
Update
ACK
Data
Data

## Slide 30: Mobile IP with reverse tunneling
Router accept often only “topological correct“ addresses (firewall!)
a packet from the MN encapsulated by the FA is now topological correct
furthermore multicast and TTL problems solved (TTL in the home network correct, but MN is to far away from the receiver)
Reverse tunneling does not solve
problems with firewalls, the reverse tunnel can be abused to circumvent security mechanisms (tunnel hijacking)
optimization of data paths, i.e. packets will be forwarded through the tunnel via the HA to a sender (double triangular routing)
The standard is backwards compatible
the extensions can be implemented easily and cooperate with current implementations without these extensions
Agent Advertisements can carry requests for reverse tunneling

## Slide 31: Reverse tunneling (RFC 3024, was: 2344)
Internet
receiver
FA
HA
MN
home network
foreign network
sender
3
2
1
1. MN sends to FA
2. FA tunnels packets to HA
by encapsulation
3. HA forwards the packet to the
receiver (standard case)
CN

## Slide 32: Problems with mobile IP
Security
  authentication with FA problematic, for the FA typically belongs to another organization
  no protocol for key management and key distribution has been standardized in the Internet
  patent and export restrictions
Firewalls
  typically mobile IP cannot be used together with firewalls, special set-ups are needed (such as reverse tunneling)
QoS
  many new reservations in case of RSVP
  tunneling makes it hard to give a flow of packets a special treatment needed for the QoS
Security, firewalls, QoS etc. are topics of current research and discussions!

## Slide 33: Traditional TCP
Congestion
Congestion Control- slow start, fast retransmit/recovery
Slow start- exponential growth, linear at later stage.
Fast retransmission- retransmission due to congestion / transmission error. sender can now retransmit the missing packet(s) before the timer expires.
Reciept of ack confirms no congestions and no need of slow start its called fast recovery from packet loss.

## Slide 34: Classical TCP Improvements Indirect TCP

## Slide 35: Snooping TCP

## Slide 36: Mobile TCP

## Slide 41
Approach | Mechanism | Advantages | Disadvantages
Indirect TCP | splits TCP connection into two connections | isolation of wireless link, simple | loss of TCP semantics, higher latency at handover
Snooping TCP | “snoops” data and acknowledgements, local retransmission | transparent for end-to- end connection, MAC integration possible | problematic with encryption, bad isolation of wireless link
M-TCP | splits TCP connection, chokes sender via window size | Maintains end-to-end semantics, handles long term and frequent disconnections | Bad isolation of wireless link, processing overhead due to bandwidth management
Fast retransmit/ fast recovery | avoids slow-start after roaming | simple and efficient | mixed layers, not transparent
Transmission/ time-out freezing | freezes TCP state at disconnect, resumes after reconnection | independent of content or encryption, works for longer interrupts | changes in TCP required, MAC dependant
Selective retransmission | retransmit only lost data | very efficient | slightly more complex receiver software, more buffer needed
Transaction oriented TCP | combine connection setup/release and data transmission | Efficient for certain applications | changes in TCP required, not transparent