## Slide 1: Module 5

## Slide 2: Overview
CN
router
HA
router
FA
Internet
router
1.
2.
3.
home
network
MN
foreign
network
4.
CN
router
HA
router
FA
Internet
router
home
network
MN
foreign
network
COA

## Slide 3: Optimization of packet forwarding
Triangular Routing
  sender sends all packets via HA to MN
  higher latency and network load
“Solutions”
  sender learns the current location of MN
  direct tunneling to this location
  HA informs a sender about the location of MN
  big security problems!
Change of FA
  packets on-the-fly during the change can be lost
  new FA informs old FA to avoid packet loss, old FA now forwards remaining packets to new FA
  this information also enables the old FA to release resources for the MN

## Slide 6: Change of foreign agent
CN
HA
FAold
FAnew
MN
MN changes location
t
Data
Data
Data
Update
ACK
Data
Data
Registration
Update
ACK
Data
Data
Data
Warning
Request
Update
ACK
Data
Data

## Slide 7: Mobile IP and IPv6
Mobile IP was developed for IPv4, but IPv6 simplifies the protocols
  security is integrated and not an add-on, authentication of registration is included
  COA can be assigned via auto-configuration (DHCPv6 is one candidate), every node has address autoconfiguration
  no need for a separate FA, all routers perform router advertisement which can be used instead of the special agent advertisement; addresses are always co-located
  MN can signal a sender directly the COA, sending via HA not needed in this case (automatic path optimization)
  „soft“ hand-over, i.e. without packet loss, between two subnets is supported
    MN sends the new COA to its old router
    the old router encapsulates all incoming packets for the MN and forwards them to the new COA
    authentication is always granted

## Slide 8: IP Micro-mobility support
Micro-mobility support:
  Efficient local handover inside a foreign domain without involving a home agent
  Reduces control traffic on backbone
  Especially needed in case of route optimization
Example approaches:
  Cellular IP
  HAWAII
  Hierarchical Mobile IP (HMIP)
Important criteria: Security Efficiency, Scalability, Transparency, Manageability

## Slide 9: Cellular IP
Operation:
  „CIP Nodes“ maintain routing entries (soft state) for MNs
  Multiple entries possible
  Routing entries updated based on packets sent by MN
CIP Gateway:
  Mobile IP tunnel endpoint
  Initial registration processing
Security provisions:
  all CIP Nodes share „network key“
  MN key: MD5(net key, IP addr)
  MN gets key upon registration
CIP Gateway
Internet
BS
MN1
data/control
packets
from MN 1
Mobile IP
BS
BS
MN2
packets from
MN2 to MN 1

## Slide 10: Cellular IP: Security
Advantages:
  Initial registration involves authentication of MNs and is processed centrally by CIP Gateway
  All control messages by MNs are authenticated
  Replay-protection (using timestamps)
Potential problems:
  MNs can directly influence routing entries
  Network key known to many entities (increases risk of compromise)
  No re-keying mechanisms for network key
  No choice of algorithm (always MD5, prefix+suffix mode)
  Proprietary mechanisms (not, e.g., IPSec AH)

## Slide 11: Cellular IP: Other issues
Advantages:
  Simple and elegant architecture
  Mostly self-configuring (little management needed)
  Integration with firewalls / private address support possible
Potential problems:
  Not transparent to MNs (additional control messages)
  Public-key encryption of MN keys may be a problem for resource-constrained MNs
  Multiple-path forwarding may cause inefficient use of available bandwidth

## Slide 12: HAWAII (Handoff Aware Wireless Access Internet Infrastructure)
Operation:
  MN obtains co-located COA and registers with HA
  Handover: MN keeps COA, new BS answers Reg. Request and updates routers
  MN views BS as foreign agent
Security provisions:
  MN-FA authentication mandatory
  Challenge/Response Extensions mandatory
BS
1
2
3
Backbone
Router
Internet
BS
MN
BS
MN
Crossover
Router
DHCP
Server
HA
DHCP
Mobile IP
Mobile IP
1
2
4
3
4

## Slide 13: HAWAII: Security
Advantages:
  Mutual authentication and C/R extensions mandatory
  Only infrastructure components can influence routing entries
Potential problems:
  Co-located COA raises DHCP security issues (DHCP has no strong authentication)
  Decentralized security-critical functionality (Mobile IP registration processing during handover) in base stations
  Authentication of HAWAII protocol messages unspecified (potential attackers: stationary nodes in foreign network)
  MN authentication requires PKI (Public Key Infrastructure) or AAA infrastructure

## Slide 14: HAWAII: Other issues
Advantages:
  Mostly transparent to MNs (MN sends/receives standard Mobile IP messages)
  Explicit support for dynamically assigned home addresses
Potential problems:
  Mixture of co-located COA and FA concepts may not be supported by some MN implementations
  No private address support possible because of co-located COA

## Slide 15: Hierarchical Mobile IPv6 (HMIPv6)
Operation:
  Network contains mobility anchor point (MAP)
    mapping of regional COA (RCOA) to link COA (LCOA)
  Upon handover, MN informs MAP only
    gets new LCOA, keeps RCOA
  HA is only contacted if MAP changes
  AR(Access Router)- Default Router
Security provisions:
  no HMIP-specific security provisions
  binding updates should be authenticated
MAP
Internet
AR
MN
AR
MN
HA
binding
update
RCOA
LCOAold
LCOAnew

## Slide 16: Hierarchical Mobile IP: Security
Advantages:
  Local COAs can be hidden, which provides some location privacy
  Direct routing between CNs sharing the same link is possible (but might be dangerous)
Potential problems:
  Decentralized security-critical functionality (handover processing) in mobility anchor points
  MNs can (must!) directly influence routing entries via binding updates (authentication necessary)

## Slide 17: Hierarchical Mobile IP: Other issues
Advantages:
  Handover requires minimum number of overall changes to routing tables
  Integration with firewalls / private address support possible
Potential problems:
  Not transparent to MNs
  Handover efficiency in wireless mobile scenarios:
    Complex MN operations
    All routing reconfiguration messages sent over wireless link

## Slide 18: DHCP: Dynamic Host Configuration Protocol
Application
  simplification of installation and maintenance of networked computers
  supplies systems with all necessary information, such as IP address, DNS server address, domain name, subnet mask, default router etc.
  enables automatic integration of systems into an Intranet or the Internet, can be used to acquire a COA for Mobile IP
Client/Server-Model
  the client sends via a MAC broadcast a request to the DHCP server (might be via a DHCP relay)
client
relay
client
server
DHCPDISCOVER
DHCPDISCOVER

## Slide 19: DHCP - protocol mechanisms
time
server
(not selected)
client
server
(selected)
initialization
collection of replies
selection of configuration
initialization completed
release
confirmation of
configuration
delete context
determine the
configuration
DHCPDISCOVER
DHCPOFFER
DHCPREQUEST (reject)
DHCPACK
DHCPRELEASE
DHCPDISCOVER
DHCPOFFER
DHCPREQUEST (options)
determine the
configuration

## Slide 20: DHCP characteristics
Server
  several servers can be configured for DHCP, coordination not yet standardized (i.e., manual configuration)
Renewal of configurations
  IP addresses have to be requested periodically, simplified protocol
Options
  available for routers, subnet mask, NTP (network time protocol) timeserver, SLP (service location protocol) directory, DNS (domain name system)
Big security problems!
  no authentication of DHCP information specified